## Slide 1: Investigating the willingness-to-wait with real-time crowding information in urban public transport
Arkadiusz Drabicki – Cracow University of Technology
dr Rafał Kucharski – Cracow University of Technology
prof. Achille Fonzone – Edinburgh Napier University
Dawid Dudek – Cracow University of Technology
prof. Andrzej Szarata – Cracow University of Technology
9th International Symposium on Travel Demand Management
Edinburgh, 19th – 21th June 2019

## Slide 2: Introduction
Overcrowding (passenger congestion) – notorious and recurrent issue in public transport networks
Despite ‘hard’ investment programmes – capacity expansion becomes eventually outstripped by the ever increasing demand pressure…
… instead – growing emphasis on ‘soft’ travel demand management strategies
ITS-fed data could be provided to passengers:
  to help them make more informed choices
  and thus improve journey experience
„I predict that when Crossrail opens in 2018 it will be immediately full. The people who predicted that it will take all the traffic out of Oxford Street or that we’ll be able to sit down on the Central Line in the rush hour will be wrong. It will just be full up with people.”
Sir Peter Hendy (2013)
Former Commissioner of Transport for London

## Slide 3: Real-time crowding information - RTCI
ITS data, gathered in real-time, could be simultaneously handled to provide information (or even prediction) on passenger flows
  increasingly feasible – APC, AFC, smart-card data, CFD…
RTCI – a fairly novel research topic:
  impact on travel behaviour…?
  proper system architecture / design…?
  consequences for PT network effectiveness…?
ITS
RTCI
- real-time
crowding information
public transport crowding

## Slide 4: RTCI and travel behaviour
How could crowding information affect passengers’ travel choices?
AND/OR
willingness to reroute towards
a less-crowded PT line
 trade-off vs. in-vehicle time
spatial shifts
temporal shifts
willingness to wait for
a less-crowded departure
of this PT line
 trade-off vs. waiting time
- ?

## Slide 5: Methodology
Focus-group discussions
Passenger surveys at bus/tram stops in the city of Krakow (Poland)
  ~ 380 respondents, ca. 2,280 SP observations
Objectives:
attitudes/preferences towards the (future) crowding information systems
  sample RTCI interpretation
SP choice survey
  propensity to wait for a less-crowded vehicle
  vs. trip- and population-related characteristics
 discrete choice model estimation
Q9. Which of these departures would you be willing to choose?
attributes:
crowding level (1st vs. 2nd trip)
waiting time for 2nd trip (5 – 10 minutes)
choice context
  journey time / service frequency
  time criticality / trip purpose
prior experience of PT crowding
sociodemographic data
  age, gender

## Slide 6: Case study – Krakow
Urban public transport (PT) system in Krakow (Poland):
population: 750k (metro area: ~ 1.4m)
core PT network: 155 [bus] and 23 [tram] lines, ca. 500k daily trips
PT vehicles: typically, increased standing space vs. reduced seating area

## Slide 7: Focus groups: how to represent RTCI?
descriptive, rating scale
  the most positive solution – clear and understandable message
  simple yet sufficient enough to make a decision
  gives a general idea how ‘bad / good’ the on-board comfort is
  adequate for short, urban PT trips
numerical scale (seats available)
  also popular, especially for long-distance trips and rail commuters
  certain credibility concerns (e.g. sudden fluctuations in no. of seats)
percentage scale
  in contrast – rather unfavourable reception so far
  ambiguous in interpretation – what does it exactly mean?
  [%] values might be perceived in terms of „gambling” risk
  increased complexity for decision-making process
7

## Slide 8: Focus groups: what kind of information from RTCI?
travel advice expected from the RTCI:
principally related to higher (over)crowding conditions:
  for time-critical trips: denial-of-boarding risk
  non-time-critical trips: ‘comfortable standing’ conditions and/or seats available
accuracy – key concern among respondents
  would this information still be valid downstream?
expectations | decision attitudes
over 50% of seats available expect a double seat just for myself | would choose this trip ‘at ease’
last few seats (< 10%) available might not get a seat | would board and wouldn’t ‘mind’ seeking a comfortable standing place
no seats available, but can stand comfortably overcrowding threshold | would take this trip, but expect some discomfort
severely overcrowded, no grip, hard to stand need to be lucky to ‘squeeze’ inside might not board | unless in a hurry – should consider different travel options

## Slide 9: SP survey results
General results – stated willingness-to-wait
with crowding information on 1st and 2nd departure…:
1st dep: no seats, but can stand comfortably
2nd dep: seats available
case no. 1

## Slide 10: SP survey results
General results – stated willingness-to-wait
with crowding information on 1st and 2nd departure…:
1st dep: overcrowded, could barely board
2nd dep: can stand comfortably
case no. 2

## Slide 11: SP survey results
General results – stated willingness-to-wait
with crowding information on 1st and 2nd departure…:
1st dep: overcrowded, could barely board
2nd dep: seats available
case no. 3

## Slide 12: SP survey results
Relevance of trip purpose and time-criticality – higher (stated) willingness-to-wait for:
non-time-critical trips (‘I don’t need to arrive on-time’)
non-obligatory trips
home-return trips
case no. 1
case no. 2
case no. 1

## Slide 13: SP survey results
Trip duration – relatively minor impact:
* majority of sampled trips no longer than 30 minutes

## Slide 14: SP survey results
The more frequent the experience of PT overcrowding, the lower the passengers’ propensity to avoid it:
How often do you experience overcrowding in your urban PT trips?
How often are you able to get a seat during your urban PT trips?
[% of respondents]
[SP answers]
* limited sample
*

## Slide 15: SP survey results
Sociodemographic characteristics:
limited propensity to wait to reduce crowding among PT commuters and those under the age of 50

## Slide 16: Choice modelling
Discrete choice model estimation based on SP results:
  BIOGEME package (Bierlaire, 2009)
  MNL (multinomial logit) model
objective – choice probability between 2 alternatives:
depart [NOW]
utility U0
[WAIT] and depart later
utility U1
OR
Waiting utility U1 calculated as a function of:
temporal utilities
  in-vehicle time
  waiting time
Boolean attributes
  RTCI of 1st vs. 2nd departure
  other trip- and population-related characteristics

## Slide 17: Choice modelling (a) – general model
depart [NOW]:
[WAIT]:
all trips |  | value | std err | t-test | p-value
βaCR case 1. |  | 0.439 | 0.234 | 1.87 | 0.0613
βbCR case 2. |  | 2.62 | 0.245 | 10.7 | 0
βcCR case 3. |  | 2.69 | 0.246 | 10.9 | 0
β IVT |  | 0.0237 | 0.00441 | 5.37 | 8.00E-08
β1 WT |  | -0.29 | 0.0215 | -13.5 | 0
β TCRIT |  | -1.41 | 0.109 | -13 | 0
β PTC |  | -0.144 | 0.141 | -1.02 | 0.306
β 65 |  | 1.92 | 0.23 | 8.35 | 0
β 50-65 |  | 0.72 | 0.242 | 2.97 | 0.00295
n = 2,280 |  |  | Rho-square: |  | 0.277
crowding level (RTCI) of 1st vs. 2nd departure (case-specific)
in-vehicle time
wait time
time-criticality
commuter (2+ trips / week)
age 65+
age 50 -65
boolean
time
boolean

## Slide 18: Choice modelling (b) – time-criticality distinguished
depart [NOW]:
[WAIT]:
time-critical trips |  | value | std err | t-test | p-value
βaCR case 1. |  | -0.218 | 0.267 | -0.819 | 0.413
βbCR case 2. |  | 1.7 | 0.252 | 6.78 | 1.23E-11
βcCR case 3. |  | 1.76 | 0.253 | 6.97 | 3.24E-12
β WT |  | -0.292 | 0.0314 | -9.31 | 0
n = 1,026 |  |  | Rho-square: |  | 0.264
non-time-critical trips |  | value | std err | t-test | p-value
βaCR case 1. |  | 0.926 | 0.217 | 4.26 | 2.07E-05
βbCR case 2. |  | 2.93 | 0.251 | 11.7 | 0
βcCR case 3. |  | 3.02 | 0.253 | 11.9 | 0
β WT |  | -0.253 | 0.0273 | -9.25 | 0
n = 1,254 |  |  | Rho-square: |  | 0.201
waiting time
RTCI of 1st vs. 2nd departure
+
boolean
time

## Slide 19: Estimation results - willingness-to-wait
MNL estimation results:
SP findings among UK rail passengers
- (Preston et al., 2017):
acceptable wait ca. 15 – 22 [mins]
VoT multipliers ~ 1.25 – 1.75 (JRT = 30 [mins])
value of time multipliers journey time = 20 [mins] | time -critical | non-time-critical
case 1. | 0.96 | 1.18
case 2. | 1.29 | 1.58
case 3. | 1.30 | 1.60

## Slide 20: Conclusions
preference towards crowding information (RTCI) in urban PT:
  simplified, descriptive representation
SP results – RTCI could induce willingness-to-wait:
  principal choice ‘trigger’ – avoid excessive (over)crowding in the 1st vehicle
  relevance of: trip purpose, propensity to arrive on-time, user characteristics…
  on average, acceptable wait of 6 – 12 [mins] for a less-crowded vehicle
applicability and future considerations:
  RTCI implementation as demand management tool (e.g. mitigating the bunching effects)
  simulation models – passengers’ choices and network performance
  stated vs. revealed choices with RTCI?
  RTCI credibility – key to its effectiveness

## Slide 21: Thank you very much for your attention!
adrabicki@pk.edu.pl
A.Fonzone@napier.ac.uk
rkucharski@pk.edu.pl
dawid.doodek@gmail.com
aszarata@pk.edu.pl
This work was supported by the STSM Grant from COST Action TU1305: Social Networks and Travel Behaviour.